SECTION 09205

PLASTER TRIM AND ACCESSORIES

Display hidden notes to specifier. (Don't know how? Click Here)

** NOTE TO SPECIFIER **  Flannery, Inc.; Plaster, stucco and drywall trim and accessory products.

.

This section is based on the products of Flannery, Inc, which is located at:

300 Parkside Dr.

San Fernando, CA 91340

Phone: 818-837-7585

Fax: 818-837-1155

Web Site: www.flannerytrim.com

Email: info@flannerytrim.com.

[click Here] for additional information.

Flannery has been at the forefront of the drywall and plaster trim industries for over 30 Years. You only have to examine our trims with Aluminum Alignment Splices to see just how innovative we are when it comes to assisting our customers. From architect to installer, Flannery is there to aid, instruct and inform. You can find and purchase Flannery products from our building material dealers throughout North America and on the web. If you have any inquiries about our products that this website cannot answer, please contact us. When you are in need of something out of the ordinary be sure to call Flannery.

GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

Plaster and stucco aluminum trim and accessories

Gypsum board aluminum trim and accessories

RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

Section 05400 - Cold-Formed Metal Framing

Section 05800 - Expansion Control: Expansion Joint Assemblies.

Section 06100 - Rough Carpentry: Framing and Blocking.

Section 07200 - Building Insulation.

Section 09220 - Plaster Assemblies.

Section 09260 - Gypsum Board Assemblies.

REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

ASTM B 244 - Standard Test Method for Measurement of Thickness of Anodic Coatings on Aluminum and of Other Nonconductive Coatings on Nonmagnetic Basis Metals with Eddy-Current Instruments.

ASTM D 1730 - Standard Practices for Preparation of Aluminum and Aluminum-Alloy Surfaces for Painting.

MIL-C-5541A - Military Specification, Chemical Conversion Coatings on Aluminum and Aluminum Alloys.

AAMA 605.2 Specification - Voluntary Specification for High Performance Organic Coatings on Architectural Extrusion Panels

AAMA 2605 – Voluntary Specification, Performance Requirements and Test Procedures for Superior Preforming Organic Coatings on Aluminum Extrusions and Panels

AA - Aluminum Association Finish Designations.

US Green Building Council.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

** NOTE TO SPECIFIER **  Delete the following paragraphs if LEED is not applicable.

LEED Submittals:  Provide documentation of how the requirements of Credit will be met:

List of proposed materials with recycled content.  Indicate post-consumer recycled content and pre-consumer recycled content for each product having recycled content.

Product data and certification letter indicating percentages by weight of post-consumer and pre-consumer recycled content for products having recycled content.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

Selection Samples:  For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

Verification Samples:  For each finish product specified, two samples, minimum size 6 inches (150 mm) square, representing actual product, color, and patterns.

Manufacturer's Certificates: Certify products meet or exceed specified requirements.

QUALITY ASSURANCE

Manufacturer Qualifications: Company specializing in manufacturing products specified in this section with minimum three years documented experience.

Installer Qualifications: Company specializing in performing Work of this section with minimum three years documented experience.

** NOTE TO SPECIFIER **  Include a mock-up if the project size and/or quality warrant taking such a precaution.  The following is one example of how a mock-up on a large project might be specified.  When deciding on the extent of the mock-up, consider all the major different types of work on the project.

Mock-Up:  Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

Finish areas designated by Architect.

Do not proceed with remaining work until workmanship, color, and sheen are approved by Architect.

Refinish mock-up area as required to produce acceptable work.

DELIVERY, STORAGE, AND HANDLING

Store products indoors in manufacturer's unopened packaging until ready for installation. Protect from damage.

PROJECT CONDITIONS

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer:  Flannery, Inc.; 300 Parkside Dr., San Fernando, CA  91340.  ASD. Phone: 818-837-7585. Fax: 818-837-1155. Web Site: www.flannerytrim.com. Email: info@flannerytrim.com.

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

** NOTE TO SPECIFIER **  Edit the following paragraphs as required and applicable to project requirements. Select trim type, shapes, prefabricated intersection and corners and ends required and delete those not required. Many sizes are available with alignment splices and venting. Verify availability with manufacturer.

ALUMINUM PLASTER TRIMS

General:

Material: Extruded aluminum alloy 6063 T5, .050 inch thick.

Provided trims in 10 foots lengths

** NOTE TO SPECIFIER ** Select the following vent slot paragraph if specified for selected trims. Select optional bug screens if required. Delete if not required.

Vent Slots: Vent slots for trims where specified are 1/8 inch wide and 1 inch long and configured at 1-1/2 inch o.c. lengthwise and 1/2 inch o. c. laterally. Each row lengthwise provides approximately 1 square inch of vented area per lineal foot.

Vent Slot Bug Screens: Provide Vented Trims with a charcoal fiberglass bug screen to prevent insects from entering the soffit area through the vent slots.

** NOTE TO SPECIFIER ** Select shape and intersection paragraphs required and delete those not required.

Plaster Control Joint: PCS 75-25-25, vertical or horizontal recessed reveal within a plaster assembly.

Sizes:

Reveal 1/4 inch by 1/4 inch, depth 3/4 inch.

Provide to size and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Straight Radius Curve

Radius Arch Radius

Reverse Arch

Intersection and Corners (Prefabricated):

Inside 90 degree Intersection

Outside 90 degree Intersection

Inside Corner

Outside Corner

Tee Intersection

4-way Intersection

** NOTE TO SPECIFIER ** Select the sizes, radius shapes, intersections and ends required and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

Plaster Screed Channel: PCS, vertical or horizontal recessed reveal within a plaster assembly.

Sizes:

PCS xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Inside Curve

Outside Curve

Reverse Arch

Arch

Intersection and Corners (Prefabricated):

Tee Intersection

4-Way Intersection

90 degree Intersection

Inside Corner

Outside Corner

Ends:

Channel End Cap

Beveled End Closure

** NOTE TO SPECIFIER ** Select the sizes, radius shapes, intersections and ends required and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

Plaster F-Mold: FPM, recessed termination reveal within a plaster assembly.

Sizes:

FPM xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Inside Curve

Outside Curve

Reverse Arch

Arch

Intersection and Corners (Prefabricated):

Inside 90 degree Intersection

Outside 90 degree Intersection

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select the sizes and intersections required and delete those not required. Reveal width and depth vary.

2-Piece Expansion Reveal: EXP, vertical or horizontal recessed expansion reveal within a plaster assembly.

Sizes:

EXP xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Intersection and Corners (Prefabricated):

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

Expansion Weep: EXPW, horizontal recessed weeping expansion reveal within a plaster assembly.

Sizes:

EXPW xx-xx

Provide to size and shapes indicated on the Drawings.

Intersection and Corners (Prefabricated):

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select the sizes and intersections required and delete those not required. Reveal width and depth vary.

Weeping Reveal: PCSW, horizontal recessed weeping reveal within a plaster assembly.

Sizes:

PCSW xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Intersection and Corners (Prefabricated):

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

No Flange Channel Screed: NF, vertical or horizontal recessed reveal within a plaster assembly.

Sizes:

NF xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

Door and Window Drip Reveal: WD. termination reveal over the top of doors and windows within a plaster assembly.

Sizes:

WD xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required.

Self-Weeping Window Drip: SWWD, drip edge over the top of doors and windows within a plaster assembly.

Sizes:

Provide to size and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes, radius shapes, intersections and ends required and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

Drip Screed: DS, drip edge and termination reveal at fascia edges within a plaster assembly.

Sizes:

DS xx-xx.

Provide to size and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Inside Curve

Outside Curve

Reverse Arch

Arch

Intersection and Corners (Prefabricated):

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

2-Piece Drip Screed: DS, drip edge and termination reveal at fascia edges within a plaster assembly.

Sizes:

DS xx-xx-2pc.

Provide to size and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

Fascia Corner Mold: FCM, termination reveal at fascia edges within a plaster assembly.

Sizes:

FCM xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

Aluminum Weep Screed: AW, foundation weep screed at the bottom of a vertical wall within a plaster assembly.

Sizes:

AW-875.

Provide to sizes and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Reverse Arch

Arch

** NOTE TO SPECIFIER ** Select the sizes intersections and ends required and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

J-Mold: JPM termination point between plaster and a dissimilar material.

Sizes:

JPM xx-xx.

Provide to size and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Inside Curve

Outside Curve

Reverse Arch

Arch

Intersection and Corners (Prefabricated):

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select the sizes and radius shapes required and delete those not required. Reveal width and depth vary. Indicated the location of vented shapes on the Drawings.

T-Mold: TPM, recessed termination reveal within a plaster assembly.

Sizes:

TPM xx-xx,

Provide to size and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Inside Curve

Outside Curve

Reverse Arch

Arch

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

Deep V-Reveal: DV, vertical or horizontal recessed reveal within a plaster assembly.

Sizes:

DV 75-150.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

Short V-Reveal: SV, vertical or horizontal recessed reveal within a plaster assembly.

Sizes:

SV xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

X-Mold: XPM, reveal at an outside corner of a plaster assembly.

Sizes:

XPM xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary.

Plaster Corner Mold: PCM, create a reveal at an outside corner of a plaster assembly.

Sizes:

PCM xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

Smooth Finish Channel: SFC, vertical or horizontal recessed reveal within a plaster assembly.

Sizes:

SFC xx-xx.

Provide to size and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select the sizes required and delete those not required. Indicate the location of vented shapes on the Drawings. Reveal width and depth vary.

Smooth Finish F-Mold: SFF. recessed termination reveal within a plaster assembly.

Sizes:

SFF xx-xx.

Provide to size and shapes indicated on the Drawings.

** NOTE TO SPECIFIER **  Edit the following paragraphs as required and applicable to project requirements. Select trim type, shapes, prefabricated intersection and corners and ends required and delete those not required. Many sizes are available with alignment splices and venting. Verify availability with manufacturer.

ALUMINUM DRYWALL TRIMS

General:

Material: Extruded aluminum alloy 6063 T5, .050 inch thick.

Provided trims in 10 foots lengths

** NOTE TO SPECIFIER ** Select the sizes, radius shapes, intersections and ends require and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

Drywall Reveal: DWR, vertical or horizontal recessed reveal within gypsum board.

Sizes:

DWR xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Straight Radius Curve

Radius Arch Radius

Reverse Arch

Intersection and Corners (Prefabricated):

Tee Intersection

4-Way Intersection

90 degree Intersection

Inside Corner

Outside Corner

Ends:

Reveal End Cap

Tapeable Reveal End Cap

** NOTE TO SPECIFIER ** Select the sizes, radius shapes, intersections and ends require and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

Drywall F Mold: DWRF, terminate gypsum board at the top or bottom of vertical walls or ceilings.

Sizes:

DWRF xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Radius Outside Curve

Radius Inside Curve

Radius Arch

Radius Reverse Arch

Intersection and Corners (Prefabricated):

Inside 90 degree Intersection

Outside 90 degree Intersection

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select the sizes, radius shapes, intersections and ends require and delete those not required. Reveal width and depth vary. Indicate the location of vented shapes on the Drawings.

Shadow Mold: DWSM, terminate gypsum board at the top or bottom of vertical walls or ceilings.

Sizes:

DWSM xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Radius Shapes: Provide to radius indicated on the Drawings.

Radius Outside Curve

Radius Inside Curve

Radius Arch

Radius Reverse Arch

Intersection and Corners (Prefabricated):

Inside 90 degree Intersection

Outside 90 degree Intersection

Inside Corner

Outside Corner

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

V Reveals: DWV, vertical or horizontal recessed reveal.

Sizes:

DWV xx-xx.

Provide to sizes and shapes indicated on the Drawings.

Intersection and Corners (Prefabricated):

Inside 90 degree Intersection

Outside 90 degree Intersection

Inside Corner

Outside Corner

Tee Intersection

4-way Intersection

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

Drywall End Enclosure: DWE, terminate walls, partitions or cased openings.

Sizes:

DWE xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

Drywall L-Metal Trim: DWL, cover unfinished edge of gypsum board.

Sizes:

DWL xxx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

Drywall Outside Corner: DOC, outside corner trim for gypsum board.

Sizes:

DOC xxx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required.

Beveled Drywall Corner: BDC, reveal at an outside corner for gypsum board.

Size:

BDC.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

Drywall Reveal Corner: DWRW, reveal at an outside corner for gypsum board.

Sizes:

DWRW xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

W-Transition Mold: WTM, termination trim for transitions between gypsum board and dissimilar material.

Sizes:

WTM xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

Drywall Ceiling Trim: DWRCT, terminate gypsum board at the top of vertical walls with gypsum board ceilings.

Sizes:

DWRCT xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER ** Select size paragraph required and delete those not required. Reveal width and depth vary.

Concealed Fastener Trim: CFT, raised feature strip over vertical gypsum board walls.

Sizes:

CFT xx-xx.

Provide to sizes and shapes indicated on the Drawings.

** NOTE TO SPECIFIER **  Edit the following paragraphs as required and applicable to project requirements. Select the finish(s) required and delete those not required.

FINISH

Mill Finish aluminum alloy 6063 T-5 for Field Priming and Painting. Do not leave exposed. Requires proper priming and painting

Anodized Finishes:

** NOTE TO SPECIFIER ** Select clear or color anodized finish and color as required and delete those not required.

Clear Anodized Finish: Architectural 200R1 medium etch (AA- M32C10A21). Thickness tested in accordance with ASTM B 244.

Color Anodizing: Two-step impregnated color Class II Architectural .40- .70 mils (AA-M12C22A33). Thickness tested in accordance with ASTM B 244.

Gold Anodized

Black Anodized

Bronze Anodized Light Bronze

Bronze Anodized Medium Bronze

Bronze Anodized Dark Bronze.

** NOTE TO SPECIFIER ** Chemical conversion coating should be specified for products to be field painted.

Chemical Conversion Coat Paint Pre-Treatment: Chem-film/Alodine Treatment conforming to ASTM D 1730 Type B and MIL-C-5541A.

Kynar Paint Finish: Two coat, oven cured 70 percent fluropolymer resin. Coating meets or exceeds AAMA 605.2 Specification “Voluntary Specification for High Performance Organic Coatings on Architectural Extrusion Panels.” Provide with a nominal dry film thickness of 1.2 mil.

** NOTE TO SPECIFIER ** Select color required paragraph required and delete those not required.

Color as selected from manufacturers standard range.

Custom Color as selected.

Custom metallic color with clear topcoat.

Powder-Coated Paint Finish: Coating meets or exceeds a dry film thickness of 1.2 mils as specified in AAMA 2605 SEC 4.3. Color uniformity meets or exceeds the requirements of AAMA 2605 SEC 7.1.

** NOTE TO SPECIFIER ** Select color required paragraph required and delete those not required.

Color as selected from manufacturers standard range.

Custom Color as selected.

EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly prepared.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

PREPARATION

Clean surfaces thoroughly prior to installation.

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

INSTALLATION

Install in accordance with manufacturer's instructions.

Installation of Exterior Plaster Trim:

Exterior Reveal Moldings Installed Vertically

Place Building Paper behind all moldings with a shiplap of 6 inches.

Attach moldings 16 inches on center to framing using approved fastening methods. Cut butt joints accurately and properly seal.

Install lath over installation flanges of all moldings.

Mask all reveals prior to plastering. Use cloth or vinyl tape specifically manufactured for masking anodized aluminum moldings. For painted moldings, use vinyl tape.

Exterior Reveal Moldings Installed Horizontally

Place building paper behind all moldings with a shiplap of at least 2 inches.

Attach moldings 16 inches or 24 inches on center to framing using approved fastening methods. Cut butt joints accurately and properly seal.

Install lath over installation flanges of all moldings.

Mask all reveals prior to plastering. Use cloth or vinyl tape specifically manufactured for masking anodized aluminum moldings. For painted moldings, use vinyl tape.

Exterior Reveal Moldings Over Metal Lath

Select molding in accordance with the plaster thickness specified.

Moldings must be tied to the lath with tie wire, to protecting the waterproof membrane. Butt joints must be cut accurately and sealed.

Cover all installation flanges of the moldings with lath.

Two layers of grade “D” paper are required by UBC when applied over wood-based sheathing.

Mask all reveals prior to plastering. Use cloth or vinyl tape specifically manufactured for masking anodized aluminum moldings. For painted moldings, use vinyl tape.

Weep, Window, and Soffit Drip Screeds

Verify installation of flashings and waterproofing for door and window openings before weeping trims are installed.

Attach weep or drip screeds horizontally 16 inches or 24 inches on center to framing using approved fastening methods. Butt joints must be cut accurately and sealed.

Install building paper or weather resistant barrier over the attachment flanges to prevent moisture from getting in behind the trim.

Install lath over attachment flanges of the molding.

For reveals, use cloth or vinyl tape specifically manufactured for masking anodized aluminum moldings prior to plastering. For painted moldings, use vinyl tape.

Vinyl Connector Clips

Use Vinyl Connector Clips for exterior aluminum trims to assist in lining up and sealing butt joints. Use vinyl connector clips as a bed for the sealant to be applied between two pieces of trim. Use Vinyl Connector Clips with Plaster Channel Screeds.

Aluminum Alignment Splices

Use Aluminum Alignment Splices and Special Corner or 90 degree Intersection Splices as required to align and join aluminum trims together along a straight plane.

Prefabricated Factory Intersections For Exterior Trims

Use prefabricated factory intersections and corners for exterior trims as required. Standard intersections or corners are provided with with 6” legs from the center point of the reveal. Installation flanges must be covered with lath and all butt joints must be sealed.

Ventilation

Provide trims with Vent Slots where specified or required to provide the needed ventilation. Vent Slots are 1/8 inch wide and 1 inch long and configured at 1-1/2 inches o.c. lengthwise and 1/2 inches o. c. laterally. Each row of Vent Slots lengthwise provides approximately one-square inch of vented area per lineal foot.

Installation of Interior Drywall Trim:

Interior Moldings with Tapeable Flanges:

Install moldings with tapeable flanges after the drywall/ gypsum board has been installed.

Framing should provide a backer so moldings can be attached with #6 drywall screws 16” on center.

Clean installation flanges before the taping. For veneer plaster flanges must be treated with a bonding agent. Mask reveals to prevent compound joint, drywall mud or texture overspray from entering the reveal opening.

Mask painted aluminum moldings with vinyl tape. Use cloth or vinyl masking tape specifically manufactured for masking anodized aluminum trims.

Do not overlap the edge of the reveal with drywall tape. Use an 8” wide trowel to apply the final skim coat.

Interior Moldings without Tapeable Flanges:

Install moldings without tapeable flanges prior to the drywall/gypsum board being installed.

Framing should provide a backer so that moldings can be attached with #6 drywall screws 16 inches on center.

Mask reveals to prevent compound joint, drywall mud or texture overspray from entering the reveal opening.

Aluminum Alignment Splices for Interior Trims:

Use Aluminum Alignment Splices for all interior trims. Use Special Corner or 90 degree Intersection Splices as needed.

Prefabricated Factory Intersections for Interior Trims:

Install prefabricated factory intersections and corners for interior trims where specified.

PROTECTION

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

SCHEDULES

** NOTE TO SPECIFIER ** Retain Paragraph below if required to suit project requirements. Identify products by name on the Drawings or use this paragraph to define the location of each type of material to be used. The following are some examples of schedule references. Edit as required to suit project or delete and identify products on the Drawings.

:

:

END OF SECTION